## Slide 1: ME 1300: Statics and Strengths
Topic Set 21
Except where otherwise noted, all imported images in these slides are from public domain sources or course textbook(s) currently or previously used in this course.

## Slide 2: Vector Transformation
Not in book

## Slide 3: Vector transformation
x
y
x’
y’
q
The *same* vector.
As seen by differently oriented observers.
Changing coordinate axes will change components,
but won’t change the vector itself.

## Slide 4: Stress Transformation

## Slide 5: Review: Parametric Plots
An ordinary plot displays x and y as functions of t individually.
A parametric plot shows (x,y) point locations as t varies.
Homework asks for ordinary plots of two functions, t(q) and s(q) individually.
Today: weplot them parametrically too!

## Slide 6: EXAMPLE

## Slide 7: Review: resolving forces on a cut plane
F(q)
N(q)
V(q)
Symbol definitions:
Abar=cross-sectional area of the bar
Acut(q)= area of the cut
P = force on the ends of the bar F(q)=force on the cut
N(q)=normal force on the cut, s(q)=normal stress on cut = N(q)/ A(q)
V(q)=shear force on the cut, t(q)=shear stress on cut = V(q)/ A(q)
Upcoming slides show that:
Formulas for A(q), F(q), N(q), and V(q) depend on whether the cutting plane is steep (slicing through the top and bottom of the bar) or shallow (slicing through the left and right ends of the bar).
Formulas for s(q) and t(q) have no similar dependencies. SEE NEXT SLIDE!

## Slide 8: How do force and stress change with changes in cut plane orientation?

## Slide 9: Alternative viewpoint
sx=P/A
and txy=0
P
P/2
P/2
P
x
y
x’
y’
Instead of thinking of this as a cut plane, let’s think of it as a coordinate system change.

## Slide 10: Plane (not plain) stress
Means that one face has no loads

## Slide 11: Example: determine normal and shear components acting on the plane AB
A
Acos60
Asin60
(350psi)(Acos60)
(500psi) (Asin60)
(350psi) (Asin60)
(sx’)(A)
(tx’y’)(A)
x’
y’
x
y
60°

## Slide 13: Vector transformation
x
y
x’
y’
q
The *same* vector.
As seen by differently oriented observers.
Changing coordinate axes will change components,
But won’t change the vector itself.

## Slide 14: Stress Transformation: same idea
The *same* stress
as seen by differently oriented observers.
Changing coordinate axes will change components, but won’t change the stress tensor itself.

## Slide 15: Stress Transformation: same idea

## Slide 16: Trig review
Multiplying this out gives a bunch of terms involving products of cosq and sinq, so you will need identities
Q: How can you remember which of the first two trig identities gets the negative sign?
A: Pick the option () that gives right answer at q=0 .

## Slide 17: Example: determine normal and shear components acting on the plane AB
x’
y’
sx=0.0
sy=-500psi
txy =350psi
q = -60deg
Read procedure for analysis in the book!

## Slide 18
Caution: the x’ axis needs to point in the 2 direction to solve this using formulas on the previous slide – you have to explain why you wouldn’t use q=30° in those formulas.

## Slide 19: Principal (not principle) Stresses

## Slide 20: Which cut plane orientation makes normal stress max? Min?

## Slide 21: Trig review
Q: If tanq=1, what is q?
A: it is either 45° or 45°+180°
Q: If tan2q=1, what is q?
A: it is either 22.5° or 22.5°+90°
ArcTan always has two solutions, each 180° apart.
Q: If tanq=0, what is q?
A: it is either 0° or 180°
Two roots!
Two roots!
Two roots!

## Slide 22: Goal: find orientation that makes normal stress min/max
Goal: find q that maximizes/minimizes
Two roots!

## Slide 23: “Principal stresses” are the max/min normal stresses
For a general angle, recall that
At the “principal” angle, where , this evaluates to

## Slide 24: Shear at the principal (not principle) angle
normal stress = C+R at one qp
= C-R at the other qp
shear stress = 0 at qp
Two roots, different by 90°!

## Slide 25: At the principal orientations normal stress is max or min, and shear stress is zero.

## Slide 26: Utes can handle the truth!
qp1
qp1
eigenvectors!
Undergrad books think you will shrivel and die if you find out that principal stresses are called eigenvalues and principal directions are eigenvectors.

## Slide 27: One vector, viewed differently.
x
y
x’
y’
q
The *same* vector.
xp
yp
qp
It’s always possible to define coordinate directions to maximize vxp
(doing so makes vyp zero)

## Slide 28: Principal directions define the special orientation where normal stress is max or min (which makes the shear stress in that orientation zero)
qp1
qp1
eigenvectors!
x
y
xp
yp

## Slide 29: Max normal stress points have zero shear (left/right extremes of circle). Max SHEAR points (top/bottom) have nonzero, but average stress! Max shear orientations are 45° off from principal directions.

## Slide 30: At what angle is shear max?
is maximized at angle
At the max shear angle (45° off from principal angle),
=R
=C

## Slide 31: Example
Laboratory orientation
Principal (max normal stress) orientation
Max shear orientation
The *same* stress state as seen by different observers.

## Slide 32
Hint: recall result from previous slide
Also recall from farther back in slides,
principal stresses= C±R
=R
=C

## Slide 33: Mohr’s Circle

## Slide 34: Two different sign conventions

## Slide 35
General Element in Planar Stress

## Slide 36
Recall: stresses seen by a rotated observer

## Slide 37
Recall: principal stresses are the normal stresses at the orientation where shear is zero

## Slide 38: Sign conventions
Stresses on a cut plane follow a different convention. They are positive if pointing this way (normal tensile and shear tending to rotate clockwise)

## Slide 39: The “x face” (normal points in x-direction)
x-face:
s=-60MPa
t=-35MPa
X-point: (-60,-35)
This slide is reiterating that tensor components follow a sign convention different from the Mohr diagram convention. The tensor shear on the x-face is positive if it points in the positive y-direction. The Mohr shear is positive if it tends to rotate the element clockwise.

## Slide 40: The “y face” (normal points in y-direction)
y-face:
s=-40MPa
t=+35MPa
Y-point: (-40,+35)
This slide is reiterating that tensor components follow a sign convention different from the Mohr diagram convention. The tensor shear on the y-face is positive if it points in the positive x-direction. The Mohr shear is positive if it tends to rotate the element clockwise.

## Slide 41
Use the X & Y points to make Mohr's Circle
Y
X
sign convention: normal stress positive if tensile
shear stress: positive if inducing a clockwise twist
Crucial! label X&Y points!

## Slide 42: Constructing Mohr’s circle
Draw stress element
Plot x-point: (s,t) with LABEL “X”.
Plot y-point: (s,t) with LABEL “Y”.
Draw line connecting the X and Y points.
Make circle with that line as diameter.

## Slide 43
Mohr's Circle Example 1
Units in MPa
x: (1,2)
y: (3,-2)
s
t
x(1,2)
y(3,-2)
y
x

## Slide 44: Generic cut plane: angles are doubled on Mohr’s circle
On Mohr’s circle the (s,t) values on this cut plane are found by going 2q ccw from the x-point!
In physical space, this generic cut plane is oriented at an angle q measured ccw from x-axis.

## Slide 45: How to draw the stress element in principal orientation
y
x
2qp
C=2
R=2.24
qp
0.24
4.24
Keep in mind: We measured ccw from x-point on circle to get to one of the principal values (marked with pink star), so we therefore also measure ccw, but half the angle, from the x-axis in the physical plane.

## Slide 46
y
x
The Fabulous Pole Point
To get the pole point on Mohr’s circle, draw a horizontal line through the x-point and a vertical line through the y-point. Label it “P.”
Lines drawn from P to any point of interest actually have the same orientation as in physical space (no confusing factors of 2).
P

## Slide 47: Using Pole point to sketch the principal orientation
y
x
qp
0.24
4.24
P
Pink line: from P to smallest principal stress. This line has the right orientation for that principal stress direction!
Green line: right orientation and value!
qp

## Slide 48
Mohr's Circle example
Prove that these two stress matrices represent the same stress state seen from different coordinate orientations, and find the orientation of the “prime” coordinate axes.
x
y
x’
y’

## Slide 49
Solution: We know that they represent the same stress state (seen from different observer orientations) because they both ended up on the same Mohr’s circle.
Getting from x to x’ on the Mohr’s circle requires moving through an angle of ArcTan(4/3) CLOCKWISE. The motion in physical space is half of this angle, and same direction.
Use the Pole Point, and it will be harder to get it wrong!
x
y
x’
y’
4
4
3
5
P

## Slide 50: Find and label the stress element with maximum shear
Units in MPa
C=1
R=5
s
t
X: (4,-4)
Y: (-2,+4)
X
Y
2qs
X’
18.4°
1
1
5
Things to note: max shear is always the radius of the circle, with direction depending on whether you choose X’ to be at the top or bottom of the circle (we picked the bottom so that X’ would be close to X).
Max shear always equals R. The corresponding stress element always has normal stresses given by C.
Contrast this with the principal stress element, which has stresses C±R but zero shears.
This distinction is often missed on exams for this class!
If you move cw on Mohr’s circle, then you move cw in physical space by an angle half as large. The Pole point can be very helpful to sort out which stress values get labeled on which axes.
P

## Slide 51
x: (0,-400)
y: (0,+400)
x’
y’
X,P
Y
s
t
x’
y’
200
346
The x’ axis is q= 15° cw from the x axis.
The X’ pnt is 2q=30° cw from the X pnt.
The y’ axis is q= 15° cw from the y axis.
The Y’ pnt is 2q=30° cw from the Y pnt.
x’
y’
200
346
How did we get the values of 346 and 200?
For that, you must work out the coordinates of the X’ point!
What are the values of shear and normal on the y’ face?
For that, you must work out the coordinates of the Y’ point!
15°
(-200,-346)
X’
30°
30°
Y’
15°

## Slide 52
Remember: rotating the cut plane’s normal (from x to x’) by an angle q (in a given direction, cw or ccw) in physical space will move you 2q (in the same direction) from the x-point on Mohr’s circle.

## Slide 53
Aside from quick estimates of stresses at other orientations, why else is Mohr’s circle awesome?