## Slide 1: ME 1300: Statics and Strengths
Topic Set 22
Except where otherwise noted, all imported images in these slides are from public domain sources or course textbook(s) currently or previously used in this course.

## Slide 2: Mohr’s Diagram for general 3D states of stress

## Slide 3: Stress tensor: 3x3 component matrix: Principal values (s1, s2, s3) define a 3D Mohr diagram
All reachable (s,t) values fall in the shaded region between disks terminating at principal stresses (eigenvalues of the
stress tensor).
(PROOF OMITTED)
t
Different cut planes or different cube orientations have different (s,t) values. They vary with cut plane orientation!
s1
s2
s3
s

## Slide 4: Plane stress: one principal stress is zero
Three possible cases for the in-plane principal stresses:
Draw the other two
circles as shown to
get the 3D diagram.
The other two principal stresses are found from the 2D in-plane part of the stress state!
t
s
t
s
t
s
Both positive
One negative and one positive
Both negative.

## Slide 5: Nearly biaxial tension
Suppose that this material fails if the maximum shear stress reaches 2MPa. Evaluate the corresponding factor of safety of this nearly biaxial tension loading.
X: (2.5,0)
Y: (3,0)
For biaxial tension (or compression), X and Y have the same (s,t) values. Let’s first look at them nearly having the same values.
t
s
1
2
3
Y
X
Z

## Slide 6: Biaxial tension
Suppose that this material fails if the maximum shear stress reaches 2MPa. Evaluate the corresponding factor of safety of this biaxial tension loading
X: (3,0)
Y: (3,0)
For biaxial tension (or compression), X and Y have the same (s,t) values, making the in-plane Mohr’s circle degenerate to a single point. That’s fine. You still make the 3D circle the same way!
t
s
1
2
3
X,Y
Z

## Slide 7
If this material fails at a shear stress of 30 ksi, what is the allowable range for sy for a safety factor of 3?
Answer:
x point
y point
These bounds keep all three Mohr’s circles below the max allowed shear, given by 30ksi divided by F.S. = 10ksi.
s
t

## Slide 8: Key lesson: Design for 3D stress even if your problem is 2D
Supplement your 2D Mohr’s circle with two more disks, each going through s=0 and through each principal value of the 2D stress state. Check if the largest disk has greater peak shear than the 2D disk.